## Slide 1: AI in Astrophotography
Dale A. Chamberlain
www.chamberlainobservatory.com

## Slide 2: What is AI (Artificial Intelligence)
Machines capable of perception, logic, and learning
Machine learning employs algorithms that learn from data to make predictions or decisions and whose performance improves when exposed to more data over time
Deep learning uses many-layered neural networks to build algorithms that find the best way to perform tasks on their own based on vast sets of data
Definition from Intel Corporation

## Slide 3: AI applications in photography
AI allows the developer to focus on solving the problem rather than coding for it
AI has been a part of digital photography for some time now
  Adobe Photoshop CC
  Topaz DeNoise AI, Gigapixel AI, Sharpen AI, etc.
  DxO DeepPrime
AI used in graphic arts
  Builds images based on a plethora of images, including stock photos by using text descriptions provided by the maker
  Not true photography
  MidJourney, StableFusion and many others
  Not what we will be discussing in this presentation

## Slide 4: Where is AI in Astrophotography?
Astrophotography has lagged behind the photography industry in adopting AI
Many astrophotographers have used Topaz Denoise AI
  Topaz Denoise AI does an excellent job for non-astrophotos but lacks features needed for astrophotography
  Topaz AI neural networks were not trained using astrophotos
Russ Croman’s RC-Astro introduced AI to astrophotography
  StarXterminator
  NoiseXterminator
  Most recently, BlurXterminator (deconvolution)
  All use neural networks built with carefully selected astro images
  The neural network is continuously learning from new images over time, and they are released to the user base as new databases

## Slide 5: What are the advantages of AI over past methods?
Again, it allows the developer to focus on solving the problem (noise reduction, deconvolution, star recognition) rather than writing code.
  Think of it as a different approach to solving the mathematical problems we face in digital image processing
Eliminates tedious guesswork in running the traditional PixInsight processes (use of masks, wavelet layers, switches and dials)
Yields much better results in much less time
Virtually free of processing artifacts
And it is using YOUR image data without replacing any part of it with another image
  Deconvolution is about recovering fine-scale image signal buried in low contrast
  It is NOT large-scale recovery such as the multiscale functions in PixInsight
  BXT only recovers detail if the detail exists in your data at low contrast

## Slide 6: Importance of PSF in BXT (Deconvolution)
The ideal point spread function (PSF) is the three-dimensional diffraction pattern of light emitted from an infinitely small point source in space and transmitted to the image plane through a high numerical aperture objective.
Think of PSF as a cone where light is diffracted through the atmosphere and an optical train, causing the light to spread beyond the center spike of the cone. Stars are selected for the PSF since they represent a tiny point of light in the overall image.
Deconvolution is never perfect, but it reduces the spread of light captured on the imaging sensor, resulting in clearer structures and tighter stars.
PSF is expressed as the FWHM (Full Width Half Maximum)

## Slide 7: Hardware
Will run on any Windows, Mac or Linux platform
Easy to install in PixInsight
Updates are automatic
Windows platforms with NVIDIA Graphics GPU will speed up processing significantly
  Install CUDA 11.8 (NOT 12.0!)
  Follow Russ Croman’s instructions on BXT for enabling CUDA support
  My image processing computer is an AMD Ryzan 9 5950 with 32 logical processors, 128GB RAM, NVMe storage and a NVIDIA RTX 3080 Graphics card

## Slide 8: Workflow Considerations
BlurXterminator (BXT) should be used early in post-processing
  After integration of images, Channel Combination, cropping, DBE/GraXpert, Color Calibration but before noise reduction while in a linear state
    AI Training was performed on images before noise reduction
  Most accurate if given the FWHM of the image rather than relying on AutoPSF
    Use Hartmut Bornemann PSFImage script on RGB
    Use PI’s FWHMEccentricity script on monochrome
  Use on luminance (either acquired or extracted)
  Can be used on RGB images – new revision allows for the selection of luminance only for RGB images
  Look Ma! No masks!
  BXT can correct aberrations caused by
    Guiding errors
    Astigmatism
    Primary and Secondary coma
    Chromatic aberrations
    Varying FWHM star diameters and halos in each color channel

## Slide 9: Workflow Considerations
NoiseXterminator (NXT)
  While in a linear state after BXT
  Immediately after permanent histogram stretching – non-linear
StarXterminator (SXT)
  Anytime when processing is better on a starless image or when a star mask is needed
  Can be done in linear and non-linear states
  Recommended to use “unscreen” mode if reblending stars back into the starless image
    PixelMath: ~((~starless)*(~stars))

## Slide 10: Links
Russ Croman’s RC-Astro site: www.rc-astro.com
Russ Croman’s AI Presentation to AIC https://www.youtube.com/watch?v=JlSUVJI93jg
Adam Block Interview with Russ Croman: https://youtu.be/6hkVBnYYlss
RC-Astro page on GPU acceleration: www.rc-astro.com/resources/gpu_nn_acceleration.php
PixInsight: www.pixinsight.com
Hartmut Bornemann scripts: www.skypixels.at/pixinsight_scripts.html
Using New Processes to Improve Image Quality in Post Processing: https://chamberlainobservatory.com/using-new-processes-to-improve-image-quality-in-post-processing/
Chamberlain Observatory: www.chamberlainobservatory.com/